## Slide 1: General Laboratory Safety
Dharmendra Singh
Safety Officer
Office of Laboratory safety and Environmental Health (OLSEH)
www.olseh.iisc.ac.in

## Slide 2: Objectives
Recognize the hazards
Assess the risks of the hazards
Minimize the risks of the hazards
Prepare for emergencies from uncontrolled hazards

## Slide 3: Contents
Personal Protective Equipment (PPE)
Safe working practices
Chemical safety
Hazardous waste
Gas safety
  Compressed gases
  Cryogens
Fire safety
Electrical safety
Laser safety
Radiation Safety
Identify hazards

## Slide 4: A. Personal Protective Equipments (PPE)
Must be worn at ALL times in the laboratory
From uvm.edu

## Slide 5: PPE: Eye Protection Options
Chemical Splash Goggles
Protects from liquid hazards
Needed in any lab that stores chemicals
Safety Glasses
Protects from mechanical and impact hazards
There are no labs in IISc that do not need these
Wear even if you are personally not working with chemicals
Face Shields
Protects from voluminous hazards
Need to be work OVER splash goggles
Must be worn in all other labs
For fuming or extremely dangerous chemicals: HF, liq. N2, etc.

## Slide 6: PPE: Eyewear Options
From AirClean Systems
Eyes are not protected
Eyes are protected
After splash
Before splash
Wear eyewear even if they fog
Get anti-fogging eyewear
Wear eyewear even if you have specs
Get a habit of wearing eyewear ALL times

## Slide 7: PPE: Nothing Should Dangle
No dangling hair, necklaces, earrings, dupattas
From WW2 safety videos
Tie-up hair or use hairnets
Avoid or tie dupattas

## Slide 8: PPE: Long Hair
Dangling hair caused Yale student Michele Dufault who was killed in an accident in April 2011
Her hair got stuck in a drill. A hair tie may have saved her life

## Slide 9: PPE: Gloves
Thin nitrile
Thick nitrile
Heat-resistant silicone
Cryogen gloves
< 2 mil thick
Solvents
Biological samples
Corrosive chemicals
Toxins
Ovens
Furnaces
Hot surfaces
Liquid N2, He, etc.
2-4 mil thick
Acids & bases
General purpose
Latex
Vinyl
Asbestos
Not allowed

## Slide 10: PPE: Gloves – Do and Don’ts
Do
Check gloves for holes or tears
Replace a torn glove
Dispose gloves in lab solid waste before leaving lab
Wash hands after using gloves
Don’t
Re-use disposable gloves
  Increased risk for contamination
Continue using a torn glove

## Slide 11: PPE: Wash You Hands!
Even if wearing gloves, always wash hands with soap after leaving the lab

## Slide 12: PPE: Footwear
No flip-flops, sandals, crocs, or chappals.
Only closed toe shoes
Common violations
  Several labs have a "take shoes off" policy.
  Some labs use chappals inside lab.
  “It is too hot to wear shoes.”
  “I was not planning to do lab work today!”

## Slide 13: PPE: Summary
From ehs.virginia.edu
Bare minimum
From indiaMART.com
Big hazards
Long sleeved thick gloves
Apron
Chemical resistant shoes
Face shield

## Slide 14: SWP: No Food in Lab
Don’t store food in lab fridge
  Not even when packed
Juice + lunch
Lab samples
Don’t eat/drink in lab
  No chai, coffee
  No mugs
  No lunchboxes
  No chewing

## Slide 15: PPE: Working with Cryogens
Mandatory PPE for filling liquid N2, Ar, and He tanks

## Slide 16: B. Safe Working Practices
Common sense rules that must be followed

## Slide 17: SWP: Never Work Alone
Follow Buddy System
  Buddy == another person in lab
Always have a buddy
  Especially at night
  Friend with a cell phone is not a “buddy”
Look out for each other
  If you see something unsafe, point it out
  Be professional, don’t take it personally
Look out for another

## Slide 18: C. Chemical Safety (CS)
Most common type of hazard and the most preventable one

## Slide 19: CS: Hazard Labels
Know Standard Hazard Symbols

## Slide 20: SWP: Material Safety Datasheet (MSDS)
Maintain hardcopy in lab

## Slide 27: CS: Chemicals Handling
www.tarleton.edu
Keep the sash as low as possible
All chemical processing in fume hoods

## Slide 28: CS: Fume Hoods
Don’t put face or head inside
Hood is not for storage
From Univ. of Waterloo
From Dow Corning Safety Presentation

## Slide 29: CS: Transporting Chemicals
Don’t carry chemicals with hands.
  Hazard to you and others
Use bottle carriers, carts with trays, buckets, etc
Avoid glass bottles

## Slide 30: CS: Always Add Acid to Water
Dilution of concentrated acid releases a lot of heat
Adding water to conc. acid releases this heat violently
  Acid can splash out of the container and onto your face
Always add conc. acid to water
Else
Acid may splash out explosively

## Slide 31: CS: Storage
Separate storage for acids; oxidizers; and bases & solvents
  Acid + solvents are explosive
  Acid + base is exothermic
  Oxidizers help combustion
At the very least use secondary containment
Chemicals stored in rated cupboards.
  Not wooden shelves
  Large solvent cupboards are exhausted
Acids
Oxidizers
Solvents & Bases
Toxins
Exhaust
Acids
Oxidizers
Solvents & Bases
Toxins
Exhaust
Segregated chemical storage
Option 1
Option 2
Secondary containment

## Slide 32: HW: Spill Response
Neutralizing kits
10-50 ml of spill
For large spills, 0.1 to 50 litres
Only by trained staff
Affected lab to be evacuated
Experienced student or staff
Large spill kits
Area must be barricaded and labelled
Emergency evacuation
For significant toxic, explosive or fire hazards
Evacuate building
Trip fire alarm

## Slide 33: D. Hazardous Waste (HW)
Don’t cook unknown soups
There is no common method of disposal

## Slide 34: HW: Segregation
Don’t throw chemicals in sewage (pH<4 or pH>10)
Accumulate segregated waste in plastic containers
Waste collected every month. For free
  http://ipc.iisc.ac.in/chem_waste_pickup.php
  Unknown waste is NOT accepted
  Most segregated and labelled waste is accepted
No chemicals down sewage
From ehs.uci.efu
No sharps in trash
From CU Boulder
Closable funnels
Solid waste
Organic
Acid
No glass in trash

## Slide 35
Chemical Waste Compatibility
From ehs.virginia.edu

## Slide 36
From Wikipedia.org

## Slide 37: HW: BioWaste
Solid bio-waste
Napkins, blood-stained wipes, etc.
Same as sanitary waste
Sharps
Syringes, needles, etc.
Sharp boxed labelled bio-waste
Wet waste
Blood or tissue/bacteria cultures
Diluted with 0.5% sodium hypochlorite solution & disposed down the drain
Carcasses
Dead rats, animals, etc.
Store in dedicated freezers
Dispose separately

## Slide 38
Cardboard?
No label
No cover
Poor upkeep

## Slide 39
LABEL YOUR CHEMICAL WASTE
Wikipedia.org

## Slide 40: E. Gas Safety (GS)
Chemical hazard combined with high-pressure hazards

## Slide 41: GS: Hazards
Hazard | Gasses
Compressed inert gas | N2, Ar, He, CO2
Flammable gasses | H2, CH4, C2H6, C2H2, LPG
Oxidizers | O2, N2O
Toxic | CO, H2S, BCl3, B2H6, Si2Cl2, GeH4, NH3
Pyrophoric (instantly catches fire in air) | SiH4, PH3,
Compressed gasses
Hazardous gases
Gas detectors
Orbital welded fittings
Gas cabinets
additional

## Slide 42: GS: Cylinder Handling
All cylinders must have tags
At least mention gas name & use-status
Cylinders must be transported on carts.
Not “rolled”
In-use cylinders must be chained
1/3
2/3

## Slide 43: SWP: Cylinder Storage
Segregate empty and filled cylinders
Full
Empty

## Slide 44: SWP: Cylinder at Point-of-USe
Regulator and valve guard
1m
Door
window
Open drain
Electrical box
5m
2m
1m
All cylinders must be used with correct regulator and valve guard
Cylinder must be placed in lab with enough exclusion zone around it.

## Slide 45: GS: Cryogens
Cryo-rated PPE
Glass dewars
Steel dewars
Compressed cylinders

## Slide 46: A Tale of Liquid Nitrogen Tank that Exploded
Safety Report:
The cylinder was standing at one end of a ~20' x 40' laboratory on the second floor of the chemistry building. It was on a tile covered 4-6" thick concrete floor, directly over a reinforced concrete beam. The explosion blew all the tile off the floor for a 5' radius around the tank turning the tile into quarter sized pieces of shrapnel that embedded themselves in the walls and doors of the lab. The blast cracked the floor but due to the presence of the supporting beam, which shattered, the floor held. Since the floor held the force of the explosion was directed upward and propelled the cylinder, sans bottom, through the concrete ceiling of the lab into the mechanical room above. It struck two 3 inch water mains and drove them and the electrical wiring above them into the concrete roof of the building, cracking it. The cylinder came to rest on the third floor leaving a neat 20" diameter hole in its wake. The entrance door and wall of the lab were blown out into the hallway, all of the remaining walls of the lab were blown 4-8" off of their foundations. All of the windows, save one that was open, were blown out into the courtyard.
-- University of Texas at Austin
Blogs.sciencemag.org/pipeline

## Slide 47
IPC Lab 2018
No tags
No restraint

## Slide 48: F: Fire Safety (FS)
Fire: the combustion reaction from interaction of HEAT + FUEL + OXYGEN
Remove any one and fire cannot spread

## Slide 49: FS: Stages of Fire

## Slide 50: FS: First Extinguishers
All labs must have them in clearly marked places
  One for each class of hazards (see next slide)
They expire. Make sure to refill/service them
  Typically need service every 3 years.
Learn how to use them. Very cheap to organize practical training on test fires

## Slide 52: FS: Fire Response
Shout
“FIRE FIRE FIRE FIRE”
Trigger fire alarm

## Slide 53: FS: Fire Response
Prepare and display an emergency exit plan
Always know the nearest exit
There should be clear signage for all fire exits

## Slide 54: FS: Fire Response
All buildings should have designated assembly points
Go to assembly area.

## Slide 55: FS: Fire Response
Only listen to a designated emergency response team
Don’t go for coffee. Stay in assembly area
We may need a headcount

## Slide 56: FS: Fire Safety Planning
All departments should have a defined Emergency Response Team (ERT)
  Among permanent faculty and staff
Typical roles/actions of ERT:
  Respond to fire/emergency
  Ensure the labs have been evacuation
  Man assembly areas
  Take attendance
  Call fire-station, security cell, ambulance, etc.
ALL incidents (big or small) must have a incident report.
  For evaluation and posterity
Organize regular mock drills.
Incident Report
ERT Composition

## Slide 57: G. Electrical Safety (ES)
Grounding, insulation, phase matching, and electrical distribution system

## Slide 58: ES: Electrical Hazards & Steps for prevention
1. Replace any worn-out or stripped wires
2. Only use 3-pin plugs
4. Power strips
  Avoid them
  Use power strips with fuse
  Calculate the load
3. Earth all equipment

## Slide 59: ES: Electrical Hazards & Steps for prevention
5. No trip hazard
7. No wet hands
8. Don’t pull cord
6. No water in vicinity
9. Don’t poke power sockets
  No jugaad please
10. Switch off

## Slide 60: H. Laser Safety (LS)
Exposure to laser light can cause significant damage to the skin and eyes – typically in the form of burns and direct damage to the retina.

## Slide 61: LS: Hazard from Laser
Exposure to laser light can cause significant damage to the skin and eyes – typically in the form of burns and direct damage to the retina.
Injury can be from direct, specular (reflected) of diffuse radiation
Direct

## Slide 62
Class | Procedure | Training | Eye Exam | Energy | Hazard
1 | Not Required | Not Required | Not Required |  | Non-hazardous to eye
1M | Not Required* | Not Required* | Not Required |  | Hazardous with collecting optics
2 | Not Required | Not Required | Not Required | < 1mW | Hazardous only when person overcomes aversion response
2M | Not Required* | Not Required* | Not Required |  | Hazardous with collecting optics and/ Class 2 hazard
3R | Not Required | Not Required | Not Required | 1 - 5mW | Hazardous when person overcomes aversion response or uses optics
3B | Required | Required | Suggested | 5 - 500mW | Direct beam eye hazard. No serious injury from diffuse reflection to eye or to skin
4 | Required | Required | Suggested | > 500mW | Hazard to eye & skin from direct, specular or diffuse reflection. Fire hazard
ONLY VALID FOR VISIBLE RADIATION

## Slide 63: LS: Effect of wavelengths of laser
Retina damage is often permanent and irreparable.
Cornea and lens damage can heal, although the injury is incredibly painful.
Retinal damage
Corneal damage
Corneal/lens damage
Notes: It is worth noting that all wavelengths over 1400nm are not equally eye-safe; light with wavelengths of around 3µm and 10µm (near the wavelength of CO2 lasers) in particular is more readily absorbed in the cornea. This results in the light being absorbed in a thin outer layer of the cornea instead of being distributed throughout the cornea, and can cause significant corneal damage at much lower exposures than other wavelengths.
Therefore, lasers emitting around 3 μm or 10 μm are less eye-safe than e.g. lasers emitting around 1.5 μm, even though they are “retina-safe”.

## Slide 64: Selecting laser safety glasses – ANSI Z136 standard
Choice of laser safety eyewear must be evaluated on case-by-case basis.
Decide on factors such as the beam path, laser parameters, and lab environment.
  Discuss your needs with your supervisor/manager
Common safety standard is ANSI Z136
OD | Transmittance
0.0 | 100%
1.0 | 10%
2.0 | 1%
3.0 | 0.1%
4.0 | 0.01%
5.0 | 0.001%
6.0 | 0.0001%
7.0 | 0.00001%
8.0 | 0.000001%
9.0 | 0.0000001%
OD = Optical Density T = Transmittance (decimal)
or
Uses OD to represent the opacity of the glasses
Valid for a given wavelength range

## Slide 65: Selecting laser safety glasses – EN207 Standard
More comprehensive than ANSI standard.
Provides an LB-Rating which has 3 components:
  Wavelength range,
  Laser mode designation, and
  Scale number (LBn)
The scale number (LBn) is used with wavelength range and laser mode to determine minimum required level of protection
  See table
Laser Mode | Engraved Symbol | Pulse Duration
Continuous Wave (CW) | D | >0.25 s
Pulsed Mode | I | >1 µs - 0.25 s
Giant Pulsed Mode | R | 1 ns - 1 µs
Mode Locked | M | < 1ns
Wavelength | Laser Mode | Maximum Power Density (P) or Maximum Energy Density (E) | Minimum Scale Number (LBn)
180 - 315 nm | D | 1x10n-3 W/m2 (1x10n-7 W/cm2) | log10(P)+3
 | I and R | 3x10n+1 J/m2 (3x10n-3 J/cm2) | log10(E/3)-1
 | M | 3x10n+10 W/m2 (3x10n+6 W/cm2) | log10(P)-10
>315 - 1400 nm | D | 1x10n+1 W/m2 (1x10n-3 W/cm2) | log10(P)-1
 | I and R | 5x10n-3 J/m2 (5x10n-7 J/cm2) | log10(E/5)+3
 | M | 1.5x10n-4 J/m2 (1.5x10n-8 J/cm2) | log10(E/1.5)+4
>1400 - 1000000 nm | D | 1x10n+3 W/m2 (1x10n-1 W/cm2) | log10(P)-3
 | I and R | 1x10n+2 J/m2 (1x10n-2 J/cm2) | log10(E)-2
 | M | 1x10n+11 W/m2 (1x10n+7 W/cm2) | log10(P)-11
Valid for a given wavelength range

## Slide 66: LS: Safe practices
Use appropriate safety eyewear whenever working near laser beams with non-negligible powers
  > Class 2 for visible lasers
  > Class 1 for invisible lasers
  Even if you personally are not using the laser
Use laser safety curtains, laser barriers and laser-blocks to prevent direct or reflected light from leaving the experimental area.
Post appropriate warning signs or labels near laser setups or rooms.

## Slide 67: LS: Safe practices
Carry out experiments on an optical table such that all laser beams travel horizontally.
Do not place laser beams at eye level.
Turn off the laser before manipulating beam path
If possible, reduce the output power of a laser during alignment procedures.
All beams should be terminated at the table
Laboratory doors should be closed whenever a laser is in use.
Be aware that lenses and other optical devices may reflect a portion of the incident beam from the front or rear surface.
No jewellery, watches, etc

## Slide 68: I: Radiation Safety (RS)
X-rays, Magnetic fields, Radioactivity, etc.

## Slide 69: RS: X-ray Protection Practices
As Low As Reasonably Achievable (ALARA)
Time
Reduce time spent with X-rays on
Track per day exposure
Distance
Keep as far as possible
Don’t loiter
Shielding
Reduce radiation to < milli Roentgens per hr.
Exposed X-ray sources and self-designed equipment may need to be registered with AERB on eLORA
Depending on the instrument, may need thermoluminescent dosimeter (TLD), a type of radiation dosimeter

## Slide 70: RS: Radioactive Materials
Use absorbent paper on all surfaces
Use appropriate shielding
Use dedicated equipment
Clearly label everything
Store material under lock and key
Keep a track of usage
Supervise visitors
Segregate waste

## Slide 71: RS: Shielding

## Slide 72: RS: Limit of exposure for Ionizing Radiation
Occupational Worker
an effective dose of 20 mSv/yr running averaged over five years
Apprenticeship & Trainee
an effective dose of 6 mSv in a year;
Public
an effective dose of 1 mSv in a year;
an effective dose of 30 mSv in any year;
an equivalent dose to the lens of the eye of 150 mSv in a year;
an equivalent dose to the extremities (hands and feet) of 500 mSv in a year
an equivalent dose to the skin of 500 mSv in a year;
an equivalent dose to the lens of the eye of 50 mSv in a year;
an equivalent dose to the extremities (hands and feet) of 150 mSv in a year and
an equivalent dose to the skin of 150 mSv in a year
an equivalent dose to the lens of the eye of 15 mSv in a year; and
an equivalent dose to the skin of 50 mSv in a year.
During pregnancy: equivalent dose limit to embryo/fetus shall be 1 mSv
AERB Directive No. 01/2011

## Slide 73: RS: High magnetic-field safety
Strong magnetic fields extend beyond strong magnets.
  Lines indicating 10‐G and 100‐G levels must be drawn on the floor of the lab. Credit and ATM cards should be kept behind the 100‐G line.
People who have pace makers should consult before entering lab
Steel, iron or other magnetic objects should be fastened down or kept behind the 100‐G line.
  Be careful with screwdrivers, wrenches and other hand tools lying around the lab
All compressed gas cylinders must be kept behind the 100G line

## Slide 74: J: Identify Hazards

## Slide 76: Find the hazards
No tags
No restraint
Blocked door
Accumulated junk
Chemicals near tank

## Slide 77
Find the hazards
Not accessible
Not accessible
Electrical wires around tank

## Slide 78
Find the hazards
Electrical boxes near tank
Exposed electrical panel

## Slide 79
Poor waste management
Storage hazard
Accumulated junk
Personal bag stored with labware
Accumulated junk

## Slide 80: Emergency Contact Details
Office of Laboratory And Environmental Health (OLSEH)
Tel No-080-22933199
email:-safety.olseh@iisc.ac.in
Security office -080-22932400
Ambulance: 080-22932234/102